# Introduction
The purpose of this document is to define the format for the Kicad schematic component library part files. This format supersedes the old file format defined in the file “library_file_format_EN.odt. The idea of component library files is no longer valid. Libraries are a collection library part files managed by some type of file structure as simple an file hierarchy on a computer to a sophisticated tool such as a version control system. Only one part can be defined per file.
This file format is based on the Specttra DSN lexer[1] work graciously coded and contributed by Dick Hollenbeck. For those not familiar with the DSN format, it is very similar the the LISP programming language in that keywords are delimited by braces. It is also known as an S-expression format. A keyword may have zero or more tokens that behave like parameters for the keyword. Tokens may be defined as additional keywords creating a programming language like structure. The decision to change to this format is to provide a more robust file lexer, a human readable file format, better file error reporting, and improved extensibility. The other driving factor is to provide a more robust format for handling the various requirements of the component library developers.
[1] See source files dsnlexer.cpp and dsnlexer.h in the Kicad source code for more information about how the DSN lexer works.
# Front Matter
This is a living document designed to be kept synchronized with the actual source code. If you modify the lexer, please update this specification as courtesy to other developers. There are many third party tools that are used to generate, manipulate, and parse component library files. Keeping this document current is vital to developers of these tools.
# Formatting
The DSN lexer enforces a strict formatting requirements. Files must be encoded in UTF8 (ASCII) format. All lexer keywords are comprised of lower case letters, numbers, and underscores. Tokens may be any alphanumeric character delimited by a white space character. Each new delimited level of keywords is indented to make files easier to read and edit with a plain text editor. Comments are supported as separate lines indented at the same level as the current keyword delimiter and begin with the # character. In line comments are not allowed.
# Using this document
This document is nothing more than several well commented part files. You should always be able to copy the text from the opening delimiter “(“ to the closing delimeter “)” into a file and open it with the library part file editor or library part viewer in Kicad's schematic capture program EESchema. It may not actually draw a useful component or be a very useful part but it should always be syntactically correct. The comments for a specific keyword always appears above the keyword it describes. Keywords defined within brackets [] are optional. A simple syntax coloring scheme has been employed to make this document more readable. Keywords are highlighted in blue, comments are highlighted in turquoise, and strings are highlighted in red.
# Logical coordinates.
The next version of EESchema and therefore the library parts will be based a coordinate system without units of measure. The advantage of having coordinates without units is any item that has an integer coordinate will be on grid. This guarantees all connectable items (pins, wires, junctions, etc.) will always get connected properly. Only non-connectable objects (arcs, text, etc.) can have non-integer coordinates. The schematic grid size determines the part coordinates in actual physical space. This allows the items to scale appropriately no matter what physical units the user selects and eliminates floating point issues when using metric coordinates in the current design.
# An example file showing syntax for all drawable item types.
# The part element is the root of the S expression used to define a library part.
# Library parts can be inherited from another part by using the extends keyword.
# The part name is the file name.
(part NAME [extends LPID]

  # Change the anchor position to something other than 0, 0. Anchor coordinates
  # must be integers.
  [(anchor (at X Y))]

  # The reference token is a reserved property. Other reserved properties are
  # value, footprint, datasheet, model, and keywords.
  [(reference REF

    # Effects define how a property is displayed. If no effect is defined then
    # the property is not displayed. Effects can also be used to override the
    # effects of a property in an inherited part. When used to override the
    # effects of an inherited property, the PROPERTY element must be defined.
    [(effects [PROPERTY]

      # Position requires an X and Y coordinates. Position coordinates can be
      # non-intergr. Angel is in degrees and defaults to 0 if not defined.
      (at X Y [ANGLE])

      # The FONT value needs to be defined. Currently, EESchema does not support
      # different fonts. In the future this feature may be implemented and at
      # that time FONT will have to be defined. Initially, only the font size and
      # style are required. Italic and bold styles are optional. The font size
      # height and width are in units yet to be determined.
      (font [FONT] (size HEIGHT WIDTH) [ITALIC] [BOLD])

      # Valid visibility values are yes and no.
      (visible YES)
    )]
  )]

  # Add a new user definable property to this part. Also can be use to override
  # a property defined in extended part.
  [(property NAME VALUE
    [(effects
      (at X Y [ANGLE])
      (font [FONT] (size HEIGHT WIDTH) [ITALIC] [BOLD])
      (visible YES)
    )]
  )]

  # Either polyline or line are can be used to define a line or series of lines.
  # Coordinates can be non-integer.
  (polyline or
  (line
    (pts (xy X Y) (xy X Y) (xy X Y) (xy X Y) (xy X Y))

    # Line widths are in units as defined above.
    (line_width WIDTH)

    # Valid fill types are none, filled, and transparent.
    (fill FILL_TYPE)
  )

  (rectangle (start X Y) (end X Y) (line_width WIDTH) (fill FILL_TYPE))

  (circle
    (center X Y)

    # Radius length is in units if defined or mils.
    (radius LENGTH)
    (line_width WIDTH)
    (fill FILL_TYPE)
  )

  (arc (pos X Y) (radius RADIUS) (start X Y) (end X Y)
    (line_width WIDTH)
    (fill FILL_TYPE)
  )

  (bezier
    (pts (xy X Y) (xy X Y) (xy X Y) (xy X Y) (xy X Y) (xy X Y))
    (line_width WIDTH)
    (fill FILL_TYPE)
  )

  (text “This is the text that gets drawn.”
    (at X Y [ANGLE])

    # Valid horizontal justification values are center, right, and left. Valid
    # vertical justification values are center, top, bottom.
    (justify HORIZONTAL_JUSTIFY VERTICAL_JUSTIFY)
    (font [FONT] (size HEIGHT WIDTH) [ITALIC] [BOLD])
    (visible YES)
    (fill FILL_TYPE)
  )

  # A pin's type is it's electrical connection. Valid connection types are
  # input, output, bidirectional, tristate, passive, unspecified, power_in,
  # power_out, open_collector, open_emitter, unconnected. Valid pin shape
  # values are none, line, inverted, clock, inverted_clk, input_low, clock_low,
  # falling_edge, and non_logic.
  (pin TYPE SHAPE

    # Pin coordinates must be integers. The angle values 0, 180, 90, and 270
    # replace the current right, left, up, and down specifiers respectively.
    # No other angles are valid.
    (at X Y [ANGLE])

    # Length of the pin in units. The pin length can be non-integer.
    (length LENGTH)
    (name “NAME” (font [FONT] (size HEIGHT WIDTH) [ITALIC] [BOLD]) (visible YES))
    (number “NUMBER” (font [FONT] (size HEIGHT WIDTH) [ITALIC] [BOLD])
      (visible YES))
    (visible YES)
  )

  # Pin merge is used to group a number of pins that are connected to the same
  # point internally to part and shows only the first pin in the list. It is
  # typically used to hide power pins on parts that have a large number of
  # power connections such as FPGAs and micro-contollers.
  [(pin_merge NUMBER1 NUMBER2 …)]

  # The pin swap hinting flag is used to indicate to an external tool ( i.e. an
  # auto router ) that the pins defined are functionally equivalent and
  # interchangeable.
  [(hint_pin_swap NUMBER1 NUMBER2 ...)]
)

# Inheritance syntax example file.
(part NAME_HINT extends LPID

  # Remove pin NUMBER defined in the base part. Only valid for extended parts.
  [(pin_del NUMBER)]

  # Swap pin NUMBER1 and pin NUMBER2 in the base part. Only valid for extended
  # parts.
  [(pin_swap NUMBER1 NUMBER2)]

  # Change the number of pin NUMBER1 to NUMBER2 in the base part. Only valid
  # for extended parts.
  [(pin_renum NUMBER1 NUMBER2)]

  # Change the name of pin NUMBER to NAME in the base part. Only valid for
  # extended parts.
  [(pin_rename NUMBER NAME)]

  # Remove property NAME from the base part. Only valid for extended parts.
  [(property_del NAME)]

  # Alternates are used to define multiple part per package devices and/or
  # alternate body styles (DeMorgan). Parts must be defined in order. There
  # can more than one alternates defined.
  [(alternates LPID [LPID...])]

  # Add a new property to this part. Also can be use to override a property
  # defined in the base part.
  [(property NAME VALUE
    [(effects (at X Y [ANGLE])
      (font [FONT] (size HEIGHT WIDTH) [ITALIC] [BOLD])
      (visible YES)]
  )]

  # The alternates swap hinting flag is used to indicate to an external tool
  # that the parts defined in the alternates list are functionally equivalent
  # and interchangeable.
  [(hint_alt_swap LPID1 LPID2 ...)]
)

# This is an example of a dual input NAND gate A of a 7400.
(part “dual_input_nand_a”
  (reference “U”)
  (arc (pos 2 0) (radius 0.4) (start 2 -4) (start_angle -90) (end 2 4)
    (end_angle 90) (line_width 0) (fill none))
  (polyline (xy 2 4) (xy -6 4) (xy -6 -4) (xy 2 -4)
    (line_width 0) (fill none))
  (pin input line (at -12 2 3.6 180)
    (name “” (font (size 1.2 1.2)) (visible yes))
    (number “1” (font (size 1.2 1.2)) (visible yes))
    (visible yes))
  (pin input line (at -12 -2 3.6)
    (name “” (font (size 1.2 1.2)) (visible yes))
    (number “2” (font (size 1.2 1.2)) (visible yes))
    (visible yes))
  (pin output line (at -12 0)
    (name “” (font (size 1.2 1.2)) (visible yes))
    (number “3” (font (size 1.2 1.2)) (visible yes))
    (visible yes))
  (pin power_in none (at -4 -4 90)
    (name “GND” (font (size 1.2 1.2)) (visible no))
    (number “7” (font (size 1.2 1.2)) (visible no))
    (visible no))
  (pin power_in none (at -4 4 90)
    (name “VCC” (font (size 1.2 1.2)) (visible no))
    (number “7” (font (size 1.2 1.2)) (visible no))
    (visible no))
  (hint_pin_swap “1” “2”)
)

# All LPIDs below this point assume that the base part is located in the same
# library as the parts that are derived from them. See the “Distributed Library
# & EESchema Parts List Design Documentation” in the Kicad source for more
# information on LPIDs.

# This is the B gate of a 7400.
(part “dual_input_nand_b” extends “dual_in_nand_a/rev1”
  (pin_del 7)
  (pin_del 14)
  (pin_renum 1 4)
  (pin_renum 2 5)
  (pin_renum 3 6)
)

# This is the C gate of a 7400.
(part “dual_input_nand_c” extends “dual_in_nand_a/rev1”
  (pin_del 7)
  (pin_del 14)
  (pin_renum 8 4)
  (pin_renum 9 5)
  (pin_renum 10 6)
)

# This is the D gate of a 7400.
(part “dual_input_nand_b” extends “dual_in_nand_a/rev1”
  (pin_del 7)
  (pin_del 14)
  (pin_renum 1 11)
  (pin_renum 2 12)
  (pin_renum 3 13)
)

# This is a DeMorgan representation of a dual input NAND gate A.
(part “dual_input_nand_demorgan_a”
  (reference “U”)
  (arc (pos -9.3 0) (radius 0.518) (start -6 4) (start_angle 50.4)
    (end -6 -4) (end_angle -50.4) (line_width 0) (fill none))
  (arc (pos -0.22 2.86) (radius 7.06) (start 0 -200) (start_angle -88.1)
    (end 6 0) (end_angle -24.6) (line_width 0) (fill none))
  (arc (pos -0.2 2.82) (radius 6.8) (start 6 0) (start_angle -24.4) (end 0 4)
    (end_angle 88.3) (line_width 0) (fill none))
  (polyline (xy -6 4) (xy 0 4) (xy 0 -4) (xy -6 -4)
    (line_width 0) (fill none))
  (pin input line (at -12 2 180) (length 6)
    (name “” (font (size 1.2 1.2)) (visible yes))
    (number “1” (font (size 1.2 1.2)) (visible yes))
    (visible yes))
  (pin input line (at -12 -2 180) (length 6)
    (name “” (font (size 1.2 1.2)) (visible yes))
    (number “2” (font (size 1.2 1.2)) (visible yes))
    (visible yes))
  (pin output line (at -12 0) (length 7.4)
    (name “” (font (size 1.2 1.2)) (visible yes))
    (number “3” (font (size 1.2 1.2)) (visible yes))
    (visible yes))
  (pin power_in none (at -4 -4 90) (length 0)
    (name “GND” (font (size 1.2 1.2)) (visible no))
    (number “7” (font (size 1.2 1.2)) (visible no))
    (visible no))
  (pin power_in none (at -4 4 90) (length 0)
    (name “VCC” (font (size 1.2 1.2)) (visible no))
    (number “7” (font (size 1.2 1.2)) (visible no))
    (visible no))
  (hint_pin_swap 1 2)
)

# This is the DeMorgan representation of gate B of a 7400.
(part “dual_input_nand_demorgan_b”
  extends “dual_in_nand_demorgan_a/rev1”
  (pin_del 7)
  (pin_del 14)
  (pin_renum 1 4)
  (pin_renum 2 5)
  (pin_renum 3 6)
  (pin_rename 1 “D”)
  (pin_rename 2 “E”)
  (pin_rename 3 “F”)
)

# This is the DeMorgan representation of gate C of a 7400.
(part “dual_input_nand_demorgan_c”
  extends “dual_in_nand_demorgan_a/rev1”
  (pin_del 7)
  (pin_del 14)
  (pin_renum 1 8)
  (pin_renum 2 9)
  (pin_renum 3 10)
)

# This is the DeMorgan representation of gate D of a 7400.
(part “dual_input_nand_demorgan_d”
  extends “dual_in_nand_demorgan_a/rev1”
  (pin_del 7)
  (pin_del 14)
  (pin_renum 1 11)
  (pin_renum 2 12)
  (pin_renum 3 13)
)

# An example of putting it all together to create a 7400.
(part “7400”
  (value “7400”)
  (alternates
    “dual_in_nand_a/rev1”
    “dual_in_nand_b/rev1”
    “dual_in_nand_c/rev1”
    “dual_in_nand_d/rev1”
  )
  (alternates
    “dual_in_nand_demorgan_a/rev1”
    “dual_in_nand_demorgan_b/rev1”
    “dual_in_nand_demorgan_c/rev1”
    “dual_in_nand_demorgan_d/rev1”
  )
  (hint_alt_swap
    “dual_in_nand_a/rev1”
    “dual_in_nand_b/rev1”
    “dual_in_nand_c/rev1”
    “dual_in_nand_d/rev1”
  )
)

# A 74LS00 is as simple as this.
(part “74LS00” extends “7400/rev1” (value “74LS00”))

# This is a so called “atomic” or “fully defined” part definition of a Texas
# Instruments part number SN74HCT00NSR.
(part “SN74HCT00NSR” extends “7400/rev1”
  (value “SN74HCT00NSR”)
  (footprint “14-SOP”)
  (datasheet “http://focus.ti.com/general/docs/lit/getliterature.tsp?genericPartNumber=sn74hct00&fileType=pdf”)
  (keywords “LOGIC” “NAND”)
  (property “Description” “IC GATE POS-NAND QD 2IN 14-SOP”)
  (property “Manufacturer” “Texas Instruments”)
  (property “Vendor” “Digikey”)
  (property “Vendor Part Number” “SN74HCT00NSR-ND”)
)