## Slide 1: OAM Header for use in Overlay Networks draft-ooamdt-rtgwg-ooam-header
Mach Chen
Yizhou Li
David Dolson
IETF-101 March 2018, London
Greg Mirsky
Nagendra Kumar
Deepak Kumar

## Slide 2: Problem statement
This document introduces Overlay Operations, Administration, and Maintenance (OOAM) Header to be used in overlay networks to create Overlay Associated Channel (OAC) to ensure that OOAM control packets are in-band with user traffic and de-multiplex OOAM protocols.

## Slide 3: Overlay Associated Channel
Associated Channel (OAC) in the overlay network is the channel that is in-band with user traffic through:
  using the same encapsulation as user traffic;
  following the same path through the underlay network as user traffic.
Creating notion of the OAC in the overlay network ensures that packets of active OAM protocols carried in the OAC are in-band with user traffic. Additionally, OAC allows development of OAM tools that, from operational point of view, function in essentially the same manner in any type of overlay.

## Slide 4: Overlay OAM Header
Header format:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| V | Msg Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Reserved | Next Prot |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ OOAM Control Packet ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 5: Requirements toward overlay encapsulation
To ensure that active OAM control packets are in-band with the monitored data flow encapsulation layer MUST comply with the following requirements:
encapsulation of OAM control message and data packets in underlay network MUST be indistinguishable from underlay network forwarding point of view;
presence of OAM control message in overlay packet MUST be unambiguously identifiable;
it MUST be possible to express entropy for underlay ECMP in overlay encapsulation in order to avoid using data packet content by underlay transient nodes.

## Slide 6
Active OAM control packet encapsulation
Underlay network encapsulation
Overlay network header
Overlay OAM header
Overlay OAM control message
Next Prot = 0

## Slide 7
Hybrid OAM control packet encapsulation
Underlay network encapsulation
Overlay network header
Overlay OAM header
Overlay OAM control message
Payload data
Next Prot = Payload

## Slide 8: Next steps
Your comments, suggestions, questions always welcome and greatly appreciated
WG adoption