## Slide 1: QoS Yang Model
http://www.ietf.org/id/draft-asechoud-rtgwg-qos-model-06.txt
IETF 102, Montreal
July, 2018
Aseem Choudhary, Norm Strahle, Ing-Whar Chen,
Mahesh Jethanandani, Ebben Aries
Notes: 1

## Slide 2: Topics
Status
Recent changes to the draft
Summary
Next Steps

## Slide 3: Status
Weekly meeting to bring closure on any feedback
Taken care of the comments provided in IETF 101
Based on the discussions, revised version:
https://tools.ietf.org/html/draft-asechoud-rtgwg-qos-model-07

## Slide 4: Recent changes to the draft
Rate is defined as value and unit. Rate unit is defined as bits/sec and percent.
Burst is defined as value and unit. Burst unit is defined as bytes and millisec.
Queues and Schedulers Model stitched to the QoS Policy Framework.
Queues can be defined as inline or as template.
Queue Policy is defined as set of queues each with associated queue parameters.
Scheduler Policy is defined as scheduling parameters with associated Queue Policy.
Queues and scheduling parameters can be defined in diffserv policy as well.

## Slide 5: Summary
The current model defines QoS framework of Policy, Classifier, Actions, Target, Queues and Schedulers
Adaptable to any vendor QoS model. The three examples of Company A, B and C models are added.
Augmentable to other Matches and Actions
Extensible through various feature definitions

## Slide 6: Next Steps
Further Comments/Input from IETF Community
Call for Adoption